## Slide 1
3 phase Squirrel Cage Induction Motor Rewinding
Prepared By:
1906152, 1906153, 1906154, 1906155, 1906156, 1906157

## Slide 2
Overview
Introduction of the project
Construction of an induction motor
Disassembling the motor into parts
Reconstructing the motor
Performing tests on the new motor

## Slide 3
What is Induction Motor
An induction motor or asynchronous motor is an AC electric motor in which the electric current in the rotor is obtained by electromagnetic induction from the magnetic field of the stator winding. The current produces a torque.
In our project, We will rewind a Squirrel Cage Induction Motor whose rated power is 325W

## Slide 4
Motor Specification(Rating)
Poles : 4
Horse Power : 0.5
Voltage Rating : 220-380 V
Current Rating : 1.0 – 1.44A
Speed : 1400 rpm

## Slide 5
Disassembling of The motor
Three main disassembling parts are:
Solid parts
Copper Wire
Rotors

## Slide 6
Disassembling of The motor(Solid parts)

## Slide 7
Disassembling of The motor(Copper Wire)

## Slide 8
Disassembling of The motor(Rotor)

## Slide 9
Wire Specification
Wire type: 100% copper
Turns per slot: 156
Wire gauge Measured: 28 Bought: 28

## Slide 10
Reconstruction of the Coils/Windings

## Slide 11
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24
A
A
B
B
Coil Placement and Connections

## Slide 12: Laboratory Test

## Slide 13: Laboratory Test Data
Test Parameters | Values
Voltage | 345 Volts
Current | 0.45 A
Power(Per-phase) | 11 watts
No Load Test
Test Parameters | Values
Voltage | 120 Volts
Current | 0.7 A
Power(Per-phase) | 39 watts
Blocked Rotor Test
Test Parameters | Values
Coil 1 | 43.7 Ω
Coil 2 | 42.6 Ω
Coil 3 | 42. 9 Ω
DC Test

## Slide 14: Equivalent Circuit Calculation
Figure Courtesy : https://www.semanticscholar.org/paper/Estimation-of-equivalent-circuit-parameters-of-and-Bhowmick-Manna/2da074f423efe631c88c21926be3510c04d618a7/figure/0
Parameters | Values
R1 | 43.067 Ω
R2 | 36.533 Ω
X1 | 23.332 Ω
X2 | 35.298 Ω
Xm | 407.337 Ω
Equivalent Circuit Parameters
Fig -1: Three phase Induction Motor Equivalent circuit referred to the Stator Side

## Slide 15: Cost Calculation
Instruments | Cost(BDT)
Motor | 1200
Insulated Copper Wire | 900
Varnish | 40
Fibre | 90
Miscellaneous | 100
Total | 2330
Costing of this Project

## Slide 16: The Reconstructed Motor

## Slide 17: Challenges Faced During this Project
Lack of Experience
No Automatic Winding Machine
Equipment Shortage

## Slide 18
Thank You